UNDERSTANDING SOLAR TERRESTRIAL REPORTS
                     PART II - INTERPRETING THE REPORTS


                                 Cary Oler

                         Solar Terrestrial Dispatch
                          University of Lethbridge



                                  _A_B_S_T_R_A_C_T

              Part I of this document series discussed the morphol-
         ogy  of  solar and geophysical phenomena.  With this back-
         ground now in hand, a discussion of the solar  terrestrial
         reports  themselves  can begin.  The purpose of this docu-
         ment is to explain the meaning of the various sections  of
         the Solar Terrestrial Forecast and Review which are posted
         over the networks on a weekly  basis.   In  addition,  the
         purpose  and  application of the other reports, alerts and
         warnings will be discussed.   After  having  digested  the
         material   in  parts  I  and  II  of  this  document,  the
         interested  reader  should  have  enough  background   and
         knowledge  to  begin  actively applying the information in
         the reports.  The reader is encouraged to digest part I of
         this  document  first  (Part I - Morphological Analysis of
         Phenomena).   It  may  be  obtained  upon   request   from
         "std_oler@hg.uleth.ca".



   December 13, 1990

































                  UNDERSTANDING SOLAR TERRESTRIAL REPORTS
                     PART II - INTERPRETING THE REPORTS


                                 Cary Oler

                         Solar Terrestrial Dispatch
                          University of Lethbridge



   _1.  _I_n_t_r_o_d_u_c_t_i_o_n

        The solar terrestrial reports posted over the networks  presently
   consist  of  five reports, alerts and warnings.  The Solar Terrestrial
   Forecast and Review is the only regular weekly publication.   It  con-
   tains  a  summary of conditions which occurred over the preceding week
   and includes forecasts for the next 10 to 20 days.  This report is the
   one  which  will  be  concentrated  on most heavily in part II of this
   document.  It contains most of the data, forecasts and charts required
   and used in practical applications.

        The Major Solar Flare Warning is a brief message which is  posted
   over  the  nets when solar physicists expect a major flare (or flares)
   to occur.  These messages are only sent when regions on the solar sur-
   face  are  complex  and  threatening enough to produce major energetic
   activity.  They are therefore only intended to  alert  people  to  the
   increased potential for major flare activity.

        A Major Flare Alert is posted whenever a  major  energetic  flare
   erupts  on the sun (of class M5.0 or greater).  Such an alert may con-
   tain a revised set of forecasts if the flare threatens to produce ter-
   restrial  impacts.   These  flare-related  alerts and warnings will be
   discussed only briefly in this document.  Their content is similar  to
   the content in the weekly forecast and review and may be applied using
   the same techniques and interpretations.

        The Major Geomagnetic Storm Alert is posted whenever  geomagnetic
   conditions reach storm levels over middle latitudes.  These alerts are
   not posted when storm conditions may exist for high latitudes, because
   high  latitudes  experience a significantly greater number of magnetic
   storms than do the  lower  latitudes.   These  alerts  may  include  a
   revised  set  of  forecasts  and charts if the storming is significant
   enough to warrant forecast revisions.  If  magnetic  storming  reaches
   levels  significant  enough  to produce possible ground-level magnetic
   induction, an Electrical Anomaly Warning may be  included  with  these
   alerts.  This will be discussed later.

        We begin our discussion of the solar terrestrial reports with  an
   analysis  of  the solar terrestrial review section of the reports.  We
   will attempt to cover the language used and discuss the format of this



                             December 13, 1990





                                   - 2 -


   section  of the reports.  Following this, we will continue with a dis-
   cussion of the Monthly Solar Terrestrial Review followed by a  discus-
   sion  of  the  Geomagnetic Storm Alerts.  The Major Solar Flare alerts
   and warnings should be more easily understood after this document  has
   been digested.

        The interested reader may need to re-read parts I and II of  this
   document  before aquiring a clearer understanding of these reports and
   their applications.  A great deal of material is covered in this docu-
   ment and may not be fully understood the first time through.  Applica-
   tion of these  reports  into  the  various  inter-related  fields  may
   require practice and persistence in order to understand the impacts of
   certain events on specific terrestrial systems (such  as  HAM  radio).
   The  interested  reader  is  encouraged to do personal research on the
   subjects of solar activity, ionospheric properties, radio  propagation
   and geophysical activity.  Research in these area's will significantly
   enhance your understanding and ability  to  interpret  and  apply  the
   information contained in the publicized reports, alerts and warnings.



   _2.  _T_h_e _S_o_l_a_r _T_e_r_r_e_s_t_r_i_a_l _F_o_r_e_c_a_s_t _a_n_d _R_e_v_i_e_w

        This report is  the  primary  report  of  solar  and  geophysical
   activity.   It  includes  enough  information and data to be of use to
   many people involved in radio communications, solar physics  and  geo-
   physics.  It is issued once a week, usually on each Saturday or Sunday
   and contains forecasts and charts for the next 10 to 20 days.

        The report itself is compiled from raw data obtained from several
   sources.   One  of the major sources is the Space Environment Services
   Center (SESC), which serves as a major global  data-collection  center
   for space-related environmental data.  The SESC is responsible for the
   solar terrestrial information which is posted on  radio  stations  WWV
   and WWVH at 18 minutes past each hour.

        The data obtained from the various sources are all collected  and
   analyzed by human hands and by computer before being compiled into the
   reports which are publically posted.  Computer  models,  coronal  maps
   and recurrent patterns are all examined and analyzed.  The results are
   incorporated into the various forecasts in the reports.

        In this section, we will begin a systematic analysis of the vari-
   ous  sections  of  the Solar Terrestrial Forecast and Review.  Some of
   the terms contained herein may not  be  clearly  defined.   For  those
   terms  which  are unclear, the interested reader is encouraged to con-
   sult the "Glossary of Solar Terrestrial Terms", available upon request
   from "std_oler@hg.uleth.ca".

   _2._1.  _S_u_m_m_a_r_y _o_f _S_o_l_a_r _T_e_r_r_e_s_t_r_i_a_l _A_c_t_i_v_i_t_y

        This section of the report summarizes the highlights of solar and
   geomagnetic activity which took place over the preceeding week.  Solar
   activity is given first, followed by  a  summary  of  geomagnetic  and



                             December 13, 1990





                                   - 3 -


   auroral  activity.  Following this, a summary of the HF and VHF propa-
   gation conditions for the preceeding week are given.  Any particularly
   severe  solar  or terrestrial activity will be given special treatment
   in this section.

        Basically, the summary of solar activity includes a discussion of
   those  regions  on the sun which exhibited abnormal signs of activity.
   This may include a description of major solar flares, noteworthy fila-
   ment  disappearances,  or  unusually large coronal holes.  It may also
   include a description of various unusual or impressive forms of  limb-
   activity  such  as  prominences,  plage  or  faculae activity, or limb
   surges or flares.

        In all of  the  solar  summaries,  references  will  be  made  to
   specific  regions  postfixed  with specific numbers (ie. Region 6354).
   These "region numbers"  are  simply  sequential  numbers  assigned  to
   active  regions  as  they  appear or are identified.  The numbering of
   these regions was started by the  SESC  many  years  ago.   The  first
   region  to  be assigned was given a region number of 1.  Consecutively
   identified regions were given numbers of 2, 3, 4 and so on.  Each  new
   region is given the next consecutive region number.

        In order for a region to be assigned a  region  number,  it  must
   qualify  according to one of the following criteria: (1) If the region
   has a sunspot group which has a first-postion  type-classification  of
   C,  D,  E, F or H, it will be given a region number (see the "Glossary
   of Solar Terrestrial Terms for a description of the sunspot  classifi-
   cation  scheme).   (2)  If two or more reports confirm the presence of
   class A or B spots (again, see the above-referenced document), it will
   be  given  a region number.  (3) If the region produces a solar flare,
   it will be given a region number.  (4) If the region  is  "bright"  in
   H-alpha light and exceeds 5 heliographic degrees in either latitude or
   longitude, it will be given a region number.  These four criteria  are
   used  in  determining what area's are assigned solar region numbers by
   the SESC and which area's are not.

        The vast majority of solar summaries include statements regarding
   the  intensity  (or  class)  of  specific  flare  events.  Flare's are
   categorized using two types  of  classifications.   The  first  method
   categorizes  a  flare  with  regards  to  it's  output energy at X-ray
   wavelengths  measured  by  orbiting  satellites.   The  second  method
   categorizes  flares  according to their size and brightness at optical
   wavelengths (observed  using  monochromatic  H-alpha  light  filters).
   Both  of these flare classifications are described fully in the "Glos-
   sary of Solar Terrestrial Terms."  Refer to it for more information.

        The positions of all solar regions and events are given according
   to  the  format:  AxxByy, where xx represents a latitude (in degrees),
   "A" represents either the "N" (North) or "S" (South) solar hemisphere,
   "yy"  represents the solar longitude given in degree's east or west of
   the central solar meridian, and "B" represents either  "E"  (East)  or
   "W"  (West)  of  this  central meridian (ie. N26E72).  The exact rota-
   tional center of the sun represents the origin where both latitude and
   longitude are measured.  The extreme limbs of the solar disk represent



                             December 13, 1990





                                   - 4 -


   longitudes of 90 degree's (either East or  West,  depending  on  which
   limb  you  look  at),  while the extreme poles of the sun represent 90
   degree's latitude (either North or South,  again  depending  on  which
   hemisphere is observed).

        It should be noted  that  the  orbit  of  the  earth  carries  us
   slightly  above  and  below  the sun's rotational equator.  During six
   months of the year, we are above the northern  portion  of  the  solar
   equator,  while during the next six months, we fall below the southern
   portion of the solar equator.  During the equinox periods (spring  and
   fall),  our orbit places us at our maximum distance above or below the
   solar equator.  If, at these times of the year, the earth  were  moved
   in  a straight line toward the center of the sun, the earth would make
   contact with the sun's surface at a latitude  of  about  7.3  degree's
   with  respect  to  the  solar  equator.  Although these periods do not
   exactly coincide with the each equinox (ie. maximum  southerly  extent
   is  achieved on 07 March, while maximum northerly extent is reached on
   09 September), they do coincide within a month of the equinox.

        These latitudinal changes are important, since it alters the  way
   we  must  observe  the sun.  During the equinox periods, the center of
   the sun as we see it is actually about 7  degree's  to  the  north  or
   south  of  the  actual  solar  equator.   If  this were not taken into
   account, the measured positions of sunspots and other surface features
   would be grossly in error.

        The important point to remember when studying  the  positions  of
   sunspot groups is that the coordinates given represent the position of
   the sunspots relative to the rotation axis of the sun as  viewed  from
   earth.   For  example, a sunspot group located at a position of N21E62
   represents a position 21 degrees north of the solar  equator,  and  62
   degrees  east  of  the solar central meridian (or 28 degrees away from
   the eastern limb [ 90 - 62 = 28 ]).

        Since the sun rotates from east to west, all sunspot  groups  and
   other  observed  features rotate in the same direction.  More specifi-
   cally, the sunspots rotate at an average speed of about 13 degrees per
   day.   So  the  sunspot  group  located  at N21E62 would be located at
   N21E49 the following day, and N21E36 the day  after  that.   They  may
   also occasionally drift in latitude, although the drift in latitude is
   negligable most of the time.

        Following the solar summary,  the  summary  for  geophysical  and
   auroral  activity  is  presented.   These  summaries  should be mostly
   self-explanatory with the exception of possible notes  regarding  mag-
   netic fluctuations.

        In summaries of particularly intense  magnetic  activity,  state-
   ments  may be made regarding the maximum intensity of some of the mag-
   netic fluctuations observed during the period being  reviewed.   These
   summaries  will  generally  involve  the terms _n_a_n_o_t_e_s_l_a and/or _g_a_m_m_a,
   which are synonymous.  The  intensity  of  magnetic  fluctuations  are
   latitude-dependent.    Higher   latitudes  naturally  experience  more
   intense magnetic fluctuations than  the  lower  latitudes.   Southerly



                             December 13, 1990





                                   - 5 -


   middle   latitude   regions  consider  magnetic  fluctuations  of  500
   nanotesla (_n_T) to be very severe, while high  latitudes  may  consider
   fluctuations  of  2500  nT  to  be  very severe.  The magnetic A and K
   indices have been developed to aid in equating the intensity  of  mag-
   netic fluctuations over wide latitudes.  For example, a magnetic fluc-
   tuation at Anchorage Alaska  may  be  considered  to  be  as  "equally
   intense"  as  a similar fluctuation in California if the A-indices for
   both locations are equal, even though  the  actual  magnitude  of  the
   fluctuations at Anchorage are much higher than the corresponding fluc-
   tuations in California.  Likewise for the K index.  A K-index of 4  at
   Yellowknife  in  northern Canada may correspond to a magnetic fluctua-
   tion of 160 nT, while a K-index value of 4  at  Boulder  Colorado  may
   correspond  to  an  actual  magnetic  fluctuation of only 50 nT.  Both
   fluctuations may be considered _e_q_u_a_l_l_y _s_e_v_e_r_e based on how often fluc-
   tuations  of that magnitude are usually encountered for that latitude.
   Yellowknife may encounter fluctuations of  50  nT  on  a  daily  basis
   whereas Boulder may not encounter magnetic fluctuations of that magni-
   tude for weeks.  Hence the need for indices  which  can  equalize  the
   latitudinal dependencies.

        Notes of auroral activity in the review section of the report are
   generally  limited  to  descriptions  as  described in the Glossary of
   Solar Terrestrial Terms.  However, for extraordinary  events  such  as
   occur  during  auroral  storms, a more detailed examination of auroral
   activity may be given.  Such descriptions may include  auroral  types,
   color  fluctuations, pulsations or movement patterns of auroral forms.
   All of these descriptions are  contained  in  the  Glossary  mentioned
   above and part I of this document.

        Notes regarding HF and VHF propagation are  usually  confined  to
   brief  accounts  of  overall  global conditions.  These conditions are
   generally rated as either above normal, normal, below normal  or  very
   poor.   Above  normal  propagation  indicates strong signals which are
   abnormally stable.  Above normal propagation is most often  associated
   with good to very good DX potentials.  Normal propagation denotes nor-
   mal conditions after considering the season and  the  position  within
   the sunspot cycle.  It is compared with the average conditions experi-
   enced over previous seasons and solar cycles.  Below  normal  propaga-
   tion  is usually associated with increased geomagnetic activity and is
   more consistent with signals of lower  quality,  less  stability,  and
   weaker  strengths.   Chances  for  DX drop noticably during periods of
   below normal propagation.  Very poor propagation is most often associ-
   ated  with magnetic storms or PCA events where signal absorption, fad-
   ing and instability dramatically affect the quality of signals.   Dur-
   ing  intense  storms,  localized  _b_l_a_c_k_o_u_t conditions may occur.  This
   term may be used in these instances to denote exceedingly high  signal
   absorption levels.

   _2._2.  _S_h_o_r_t _T_e_r_m _S_o_l_a_r _T_e_r_r_e_s_t_r_i_a_l _F_o_r_e_c_a_s_t

        This section of the report follows the same  basic  structure  as
   the  review described in the last section, except that predictions are
   given instead of reviews.  The predictions are  made  using  the  same
   methods  described  in the preceding sections, but are translated from



                             December 13, 1990





                                   - 6 -


   tables and charts into sentence form.

        This short-term prediction section is intended to point  out  the
   highlights which can be expected over the coming week.  Overall global
   conditions are given in this section of the  report.   Therefore,  the
   person  interested  in radio communications or auroral activity should
   keep in mind the nature of this section.  It is not intended  to  list
   the  possible localized phenomena which might occur.  Just the general
   overall global conditions are stated.

        The short term forecasts should be used as a guide only.  The art
   of  predicting  geomagnetic  storms and major flares is by no means an
   easy  process.   There  are  many  variables  which  are  unknown  and
   processes  which  are not fully understood yet.  Although we have made
   great advancements in the fields of solar physics and  geophysics,  we
   have  a  long  way  to  go  in the area of predictions.  The forecasts
   presented in these reports may therefore be in error at  times.   They
   are,  however,  based  on  the most current models and the most recent
   data.

   _2._3.  _S_o_l_a_r _R_e_g_i_o_n _S_u_m_m_a_r_y

        The summary of solar regions is the section of the  report  which
   is  in  tabular  form  and includes the region numbers, sunspot sizes,
   sunspot classes, angular extents, magnetic configuration,  etc.   This
   section  is of great value to those who are tracking sunspot groups or
   watching for signs of growth or increased magnetic  complexity  and/or
   flaring.

        Although each of the aspects of this table are described  in  the
   Glossary  of Solar Terrestrial Terms, we will elaborate on some of the
   more vague terms of in this section.

        Each solar region is given a number and its position on the solar
   disk  is  measured  (as  was  described  above).   This identifies and
   defines the exact position of a solar region on the  sun.   The  posi-
   tional  description  (ie. the latitude/longitude description) is rela-
   tive to the hemisphere of the sun which is  in  view.   That  is,  the
   longitude  of  a solar region is relative to the center of rotation as
   seen from the earth.  This places the 00  degree  longitude  (ie.  the
   central  meridian)  continuously  at  the center of the sun (in a line
   stretching from the north solar pole through the center of the disk as
   observed  from  the earth, to the south solar pole).  All of the solar
   regions rotate while the longitudinal lines remain  stationary.   This
   method  of  marking  positions of sunspots and other phenomena is very
   adequate, but fails to describe the position of sunspots  on  a  solar
   global  basis  with  respect to a fixed 360 degree longitudinal system
   (as is employed for the earth).

        In order to solve this problem, a system was developed  to  begin
   mapping  active  regions  on  a  fixed  solar geographical basis.  The
   actual longitudinal position of sunspots are therefore recorded in two
   different  ways.   The first way (described in the preceding sections)
   enables us to determine how far  away  a  solar  region  is  from  the



                             December 13, 1990





                                   - 7 -


   central  meridian.  It effectively separates the observable solar disk
   into an east and a west hemisphere with the dividing  line  coinciding
   with  the  central  solar meridian.  The second method is analagous to
   the way we have mapped our earth, with fixed lines of longitude divid-
   ing up the entire sphere.

        The  figures  in  the  region  summary  under  the  heading  "_L_O"
   represent this second mapping method.  This second method is useful in
   determining the movement of a sunspot region compared to the  flow  of
   gases  around  the  sunspot  region.   Sometimes,  sunspots  will move
   slightly slower than the gases around the spot, which  will  gradually
   cause  the longitudinal location of the sunspot to change.  Sometimes,
   they move faster than the gases normally do at that location.   So  by
   observing  these longitudinal values, you can determine whether a sun-
   spot is moving faster or slower than usual.

        This method of referencing sunspots is also useful in identifying
   regions  of  the sun which are abnormally active.  During the years of
   maximum solar activity, the sun often  exhibits  longitudinal  regions
   which  are  more  active  than other longitudes.  During solar maximum
   years, there are often two areas of  abnormal  activity  separated  by
   about  180 degrees.  By observing the positions of sunspots using this
   method of mapping, the active  solar  longitudes  can  be  discovered.
   This is valuable for those who want to forecast solar activity.  Like-
   wise, some solar longitudes are often regions of enhanced  corpuscular
   emissions  (ie.  regions  where matter is ejected from the sun), which
   can  significantly  affect  radio   communications   and   geomagnetic
   activity.   Plotting the positions of these active longitudes can also
   be of tremendous aid in predicting  recurrent  storms  or  periods  of
   increased geophysical activity.

        The column in the table labelled "_Z" represents an optical  clas-
   sification  scheme  for  sunspots  and sunspot groups.  The details of
   this classification method are given in the Glossary of Solar  Terres-
   trial  Terms.  The interested reader is directed to consult this docu-
   ment for more information.  It categorizes the optical shape and  com-
   plexity of sunspot groups.

        The column labelled "_L_L" represents the  angular  extent  of  the
   sunspot  group.   Angular extent is given in solar degrees.  Comparing
   this value with the number of spots within the region (denoted by  the
   "_N_N"  column  of the table) yields the density of the group.  The den-
   sity is important because it is an indirect measure of  the  gradients
   of  magnetic  fields  within  the region.  High gradients produce more
   frequent and more severe solar flares, while weak gradients  are  usu-
   ally  associated  with  less-compact  spot  groups  which produce less
   severe and less frequent flares.

        The "_M_A_G _T_Y_P_E" or magnetic-type of sunspot groups as noted in the
   last  column  of  the table can also be used to determine the magnetic
   complexity and magnetic gradients within active regions.  Consult  the
   Glossary mentioned above for more information regarding these classif-
   ications.




                             December 13, 1990





                                   - 8 -


        In addition to details on spot groups, this region of the  report
   also  enumerates  those area's which are _n_o_t associated with sunspots,
   but contain area's of enhanced  H-alpha  plages.   These  regions  are
   assigned  region  numbers  according  to the rules noted above.  These
   regions are often the sites for sunspot formation.  They may  also  be
   associated with old regions which are decaying.

   _2._4.  _G_e_o_m_a_g_n_e_t_i_c _A_c_t_i_v_i_t_y _S_u_m_m_a_r_y

        Following the solar  region  summary,  a  graphical  analysis  of
   recent geomagnetic activity is presented.  This graphical table charts
   geomagnetic activity as it is recorded for Boulder Colorado,  for  the
   last  87  hours  up to the time the report was compiled.  The activity
   for Boulder is chosen because it represents a middle latitude  station
   and  should  experience  magnetic activity similar to other regions in
   similar latitude zones.  It is also a good point of reference.

        Magnetic activity along the same latitude band as Boulder  should
   be similar.  Locations to the north of this latitude band will tend to
   experience greater geomagnetic activity, while locations to the  south
   of  this  latitude  zone  will  tend  to  experience  less geomagnetic
   activity.  When reading this chart, it  is  important  to  keep  these
   things in mind, since geomagnetic activity is very latitude dependent.

        This chart has been constructed from each of the 3-hourly K-index
   values  reported  by Boulder over the period in the chart.  Each graph
   line, therefore, represents a 3-hour period of time.  The time on this
   graph  is  in local time for area's in North America.  For Europe, the
   date lines (ie.  the lines separating days  of  the  week)  should  be
   shifted  left  by  about three positions.  Area's to the west of North
   America (ie. Hawaii, Japan, etc.) should shift the date lines  to  the
   right between two and three positions.  The first graph line following
   a date line represents the magnetic activity that was  experienced  up
   to midnight local time for area's over North America.  This same graph
   line would represent  the  magnetic  activity  which  was  experienced
   between  3 am and 6 am local time for area's near Great Britain.  This
   time change is due to the dependence of the chart on _l_o_c_a_l _t_i_m_e.

        The left-hand side of the chart relates the levels of geomagnetic
   activity  to the approximate corresponding severity of activity.  This
   activity is defined from "Very Quiet"  levels,  which  corresponds  to
   magnetic  K-indices  of  zero,  to  "Extremely  Severe"  levels  which
   corresponds to magnetic K-indices of about nine.

        The right-hand side of this chart serves as a _v_e_r_y _r_o_u_g_h _g_u_i_d_e to
   the potential severity of magnetic-induction that _m_i_g_h_t be experienced
   during corresponding levels of magnetic activity.  By "magnetic induc-
   tion,"  we  mean  the  severity  of magnetic fluctuations necessary to
   begin influencing ground-based systems such  as  electrical  powerline
   systems, telecommunications systems, pipeline networks, etc.  This end
   of the chart is not intended to be a  definitive  classification,  but
   rather  is  only  meant  to serve as a _p_o_t_e_n_t_i_a_l indicator to possible
   magnetic-induction.  There are a great many  variables  that  must  be
   taken  into  account before magnetic fluctuations can be qualitatively



                             December 13, 1990





                                   - 9 -


   classified as capable of inducing  electrical  currents  into  ground-
   based  systems.   These  variables  are  not considered in this chart.
   Only the general level of magnetic fluctuations are considered and are
   related  to possible magnetic induction.  Such localized parameters as
   air-earth conductivity, ionospheric current system parameters,  local-
   ized  rate  of change of magnetic intensities, and ground-based system
   network configurations relative to the direction of magnetic  fluctua-
   tions  must  be  considered  (among  other things) before true hazards
   regarding magnetic induction can be determined.  Therefore, this  area
   of  the chart should be used only as a very rough guide.  Nothing more
   and nothing less.  It should be noted, however, that magnetic fluctua-
   tions  rated  as  K-indices greater than 7 generally become capable of
   wide-spread electrical current induction.   Storms  with  fluctuations
   this high are usually capable of influencing ground-based systems over
   wide areas.

        The magnetic field graphed in this chart represents the _p_e_a_k mag-
   netic  activity  observed  at Boulder Colorado.  It does _n_o_t represent
   average magnetic activity.  This is important to realize.  As noted in
   part  I  of  this  document, the magnetic field consists of three com-
   ponents.  Each of these three components are monitored  by  magnetome-
   ters  at  Boulder.  At the end of each three hour interval, the traces
   produced by these magnetometers are examined and the trace  containing
   the greatest perturbation is selected.  The selected magnetic fluctua-
   tion is then converted into K-index form.  This is the value which  is
   reported by radio stations WWV and WWVH.  This is also the value which
   is graphed in this section of the report.

   _2._5.  _1_0-_D_a_y _G_e_o_m_a_g_n_e_t_i_c _A_c_t_i_v_i_t_y _F_o_r_e_c_a_s_t

        This chart graphs the expected  levels  of  geomagnetic  activity
   over  a  10-day  period.  Each day is separated into three 8-hour seg-
   ments.  Each line of the chart therefore  represents  one  eight  hour
   interval  of  time.  This chart graphs expected conditions relative to
   _U_n_i_v_e_r_s_a_l _T_i_m_e.  That is, the first line after each date dividing line
   represents  expected  conditions between 00 UT and 08 UT for that day.
   The middle graph line represents conditions expected between 08 UT and
   16  UT.   The last graph line for each day in the chart represents the
   magnetic activity that is expected from 16 UT to 24  UT.   This  chart
   should  be  more  easily  interpreted  than  the  previous geomagnetic
   activity summary chart.

        The predictions are based on data regarding coronal holes, poten-
   tial lunar interactions, recurrent activity, diurnal trends and poten-
   tial solar activity influences.

        This prediction chart also defines the _p_e_a_k _p_l_a_n_e_t_a_r_y geomagnetic
   activity  levels.   This differs from the previous chart which summar-
   ized geomagnetic activity at Boulder.  This prediction  chart  differs
   in  that _p_l_a_n_e_t_a_r_y magnetic conditions are given, rather than the con-
   ditions for a specific location or region.






                             December 13, 1990





                                   - 10 -


   _2._6.  _G_r_a_p_h_i_c_a_l _A_n_a_l_y_s_i_s _o_f _S_o_l_a_r _A_c_t_i_v_i_t_y

        The graphical chart summarizing solar activity is  produced  each
   week for a 60-day period.  This period covers two complete solar rota-
   tions and is sufficient to show the cyclic behavior of solar  activity
   from one cycle to another.

        The solar flux (the intensity of solar radio  noise  observed  at
   10.7  cm  wavelengths)  is  plotted  in this graphical analysis.   The
   solar flux represents the slowly varying component  of  the  sun  (see
   part  I)  and  is strongly correlated with the number and intensity of
   sunspot groups on the solar surface.  The higher the  number  of  sun-
   spots  visible,  the  higher  the  solar  flux.  As sunspots disappear
   behind the western solar limb, the solar flux decreases.  The 10.7  cm
   solar radio flux is therefore a good indicator of the overall state of
   the observed solar environment.

        Under normal conditions, the plot lines for the  solar  flux  are
   plotted  using  asterisks  (*).   However,  on day's when major flares
   erupt, these plot lines are changed from  asterisks  to  "F"'s.   This
   enables readers to determine at what time solar flares occurred during
   the rotational cycle of the sun.  In most cases, it will  be  observed
   that  most  of  the  major flare activity occurs during the rotational
   peak of each cycle.  There are, however, exceptions to this,  as  will
   occasionally be noted.

        Plot lines are only changed from  asterisks  to  F's  when  major
   flares erupt which meet or exceed an X-ray intensity of class M5.0.  A
   flare of class M4.9 may be a fairly major event, but is not considered
   a  major  class  flare  since it never reached M5.0 class intensities.
   Most flares, however, are either above or notably  below  this  limit.
   There  are  many  more  flare's of class M3.0 intensity than there are
   flare's of class M4.0 intensity.  Most major  flares,  therefore,  are
   observed  to  occur  above  this  M5.0 transition level.  Very few are
   borderline cases.

   _2._7.  _2_0-_D_a_y _S_o_l_a_r _A_c_t_i_v_i_t_y _F_o_r_e_c_a_s_t

        The 20-day solar activity forecast chart is constructed based  on
   the  activity  which  was  observed  over previous solar rotations, in
   addition to the status of the regions which are currently  visible  on
   the  sun.   The  intensity, size and number of sunspots in each region
   are all analyzed (among other things) before this prediction chart  is
   produced.

        The plot lines of this chart  represent  the  solar  flux  levels
   which  are  expected  to occur throughout the 20-day period covered by
   the chart.  The actual flux values will  frequently  differ  from  the
   actual  flux  values  observed, since predicting the activity of solar
   regions is still very difficult to do beyond  approximately  three  to
   four  days.  Regions behind the sun may be developing which could sig-
   nificantly alter the shape of the prediction  charts.   These  regions
   cannot  be seen or detected in any way until they approach the eastern
   limb of the sun.  Hence, these solar activity  predictions  should  be



                             December 13, 1990





                                   - 11 -


   used only as a guide.  The predictions are generally good at forecast-
   ing the times when the solar flux will peak or reach its minimum  dur-
   ing  a rotational cycle, and this can be of tremendous value to people
   interested in the level of ionospheric ionization  which  is  strongly
   proportional to the solar flux.

        Flare's are not included in this prediction  of  solar  activity.
   Flares  are  extremely difficult to predict, even when considering the
   short-term.  Our knowledge of flares has exploded since the early part
   of  this  century.   However, our knowledge is still not sufficient to
   reliably predict the occurrence of major flares over periods in excess
   of  several days. Therefore, this graphical solar activity forecast is
   limited to a treatment of the solar flux _o_n_l_y.  As far as  flares  go,
   an  increasing  solar  flux  generally  increases  the  risk for major
   flares.  The higher the solar flux values, the greater  the  risk  for
   major  flares,  since the solar flux is directly related to the number
   and intensity of active regions on the sun.

   _2._8.  _H_F _R_a_d_i_o _S_i_g_n_a_l _P_r_o_p_a_g_a_t_i_o_n _P_r_e_d_i_c_t_i_o_n_s

        This  section  of  the  Solar  Terrestrial  Forecast  and  Review
   involves  the  propagation  of  high-frequency  (HF)  radio waves over
   long-distances.  It is a forecast of the expected quality of HF  radio
   signals travelling over long-distances.

        The quality of radio signals  is  divided  into  several  area's.
   Radio  signals  which  have  outstanding  strength  and stability over
   long-distances are categorized as  _e_x_c_e_l_l_e_n_t.   These  conditions  are
   rarely  observed  and  occur  more frequently over the lower latitudes
   than the higher latitudes.  Signals which are  abnormally  strong  and
   stable  over  long-distances  are  classified as _v_e_r_y _g_o_o_d.  These are
   above-normal conditions when considering the  time  of  year  and  the
   state  of  the  solar cycle.  Signals which are normal for the current
   season and state of the solar cycle are given a  _g_o_o_d  classification.
   These  signals  are generally stable and relatively strong considering
   the time of year, but may suffer  some  minor  fading  or  distortion.
   Noise  may  also  be somewhat of a factor, but is generally tolerable.
   When signals fall below the normal quality, they may be categorized as
   _p_o_o_r.   Poor radio signals over long distances are those which experi-
   ence strong fading or  flutter,  abnormal  levels  of  absorption,  or
   increased  levels  of  noise (or any combination of the above).  Long-
   distance propagation is still usually possible  in  these  cases,  but
   suffer  significantly  increased levels of distortion which may hamper
   attempts at long-distance voice contacts.  _V_e_r_y _p_o_o_r radio signal pro-
   pagation  occurs  when  signals  experience severe fading and flutter,
   high levels of absorption, high levels of noise  and  high  levels  of
   distortion  (or any combination of the above).  Long-distance communi-
   cation usually becomes very difficult during these periods and may not
   be  possible  at all over some regions.  When radio signals are unable
   to be propagated at all over long distances, or  are  very  poor  over
   short to moderate distances, communication is rated as being _e_x_t_r_e_m_e_l_y
   _p_o_o_r.  This category will only usually be encountered at higher  lati-
   tudes and during periods of intense geomagnetic storming.




                             December 13, 1990





                                   - 12 -


        In these forecasts, each day is composed of three  8-hour  inter-
   vals.   Since  these  forecasts are also _U_T-_c_o_r_r_e_l_a_t_e_d, the first plot
   line of each day represents the interval between 00 UT and 08 UT.

        There is one _v_e_r_y _i_m_p_o_r_t_a_n_t note which should  be  understood  by
   all  those  who  use  these  forecasts  as  guides.  The local time of
   attempted communications is a very important factor  in  long-distance
   communications.  This factor is _n_o_t considered in these forecasts, nor
   could it be easily incorporated into these  charts.   The  charts  are
   intended to be _g_l_o_b_a_l_l_y valid. Hence, the obvious diurnal enhancements
   which occur cannot be included in this global  forecast.   The  person
   interested  in  radio  communications  is  already  expected to have a
   knowledge of the diurnal enhancements for his or  her  region.   These
   charts,  therefore, are only intended to aid the interested communica-
   tions operator in determining the potential times when enhanced  radio
   communications  may  be  possible.   It is not intended to reflect the
   diurnal enhancements which occur, unless the enhancements are signifi-
   cant.

        The forecasts are based  heavily  on  recurrent  geomagnetic  and
   auroral activity, which are primary factors in determining the quality
   of radio signal propagation conditions.  The intensity  of  ionization
   of the appropriate ionospheric layers are also examined when preparing
   these charts.

        This section is separated into three charts for the high latitude
   regions,  middle  latitudes  and  the  low  latitude  regions.  Global
   separation of area's into latitudinal  zones  is  required  since  the
   characteristics  and  quality of radio propagation differ from zone to
   zone.

        To make the best use of these charts, the  interested  reader  is
   encouraged  to  follow this procedure.  Determine the path endpoint of
   your signal.  That is, determine the  location  where  you  want  your
   transmitted  signal to be received.  This is the _p_a_t_h _e_n_d_p_o_i_n_t or _d_e_s_-
   _t_i_n_a_t_i_o_n.  Your transmitter location is the _s_t_a_r_t_p_o_i_n_t or _s_o_u_r_c_e.  Now
   draw  a  great-circle  between the startpoint and the endpoint.  Next,
   determine the most _n_o_r_t_h_e_r_l_y geographical coordinates  of  the  great-
   circle  connecting  the startpoint and the endpoint (we will call this
   point the _n_o_r_t_h_p_o_i_n_t) and note  the  UT  time  of  your  transmission.
   After  calculating  this  information, determine what latitudinal zone
   the path northpoint lies in.   Finally,  consult  the  HF  propagation
   prediction   charts   and  select  the  latitudinal  zone  chart  that
   corresponds to the _l_a_t_i_t_u_d_e _o_f _t_h_e _p_a_t_h _n_o_r_t_h_p_o_i_n_t.  Using the UT time
   of the transmission, select the appropriate day in the chart and exam-
   ine the plot line which corresponds to the UT time  of  the  transmis-
   sion.   This  is the propagation quality that can be expected for that
   path at that time. Note, however, that  you  must  also  consider  the
   local  time  of day of your transmission, and the local time of day at
   the path endpoint in order to determine  the  diurnal  characteristics
   that  should  be  expected.   This  information  is not given in these
   charts, but should already be known by the radio operator who is fami-
   liar  with  the diurnal conditions which occur at his or her site.  In
   order to be most accurate, this diurnal component must  be  considered



                             December 13, 1990





                                   - 13 -


   together   with  the  propagation  predictions.   Therefore,  if  your
   transmission were conducted during a period of time when you know your
   signal  is enhanced, a truer representation of the propagation quality
   may be obtained by examining the prediction charts (using  the  method
   above)  and  increasing  the quality of propagation up by _n_o _m_o_r_e than
   one level (ie. from "fair" to "good").

        For example, suppose you wanted to  communicate  between  Florida
   and  Great  Britain.  Florida is a low latitude zone and Great Britain
   is a middle-latitude zone.  Next,  we  draw  a  great  circle  between
   Florida  and  Great Britain.  If you have no numerical method of doing
   this, you can approximate the great circle path by stretching a narrow
   piece of paper on a globe of the world such that the ends of the piece
   of paper intersect the path startpoint and endpoint (the paper  should
   be  bent  so  that  one  of  its edges lays flat on the surface of the
   globe).  The path that this paper makes on the globe  will  be  curved
   and  represents  the  great-circle path between Florida and Great Bri-
   tain.  By examining the great circle path, we are able to see that the
   most  northerly geographical position on the path is at Great Britain.
   Since Great Britain is a middle-latitude region, we consult the middle
   latitude  prediction  chart.  If you were to transmit to Great Britain
   at 10:00 UT on Thursday, you would examine the middle plot line of the
   middle-latitude  prediction  chart  for  Thursday.   Since 10:00 UT in
   Florida is near the time the sun rises, you might  expect  propagation
   conditions  to  be enhanced somewhat (depending on your location, time
   of year, etc.).  If this were the  case,  the  prediction  charts  may
   underestimate  the quality of propagation you might expect during that
   period.  On the other hand, if the time were about  05:00  UT  Florida
   time,  conditions  might  be worse than those suggested by the charts.
   So local time at the startpoint and endpoint are both  important  when
   determining  possible  diurnal  influences  and  might need to be con-
   sidered.

        In many cases, the great-circle path of  the  signal  may  travel
   over  more  northerly latitudes than the startpoint and endpoint.  For
   example, a transmission between central Canada and Great  Britain  may
   result  in  a  great-circle path that passes through the high-latitude
   regions before reaching Great Britain, even though both the startpoint
   and  endpoint  are middle-latitude stations.  In these cases, the most
   northerly position of the great-circle path should be used.

        If the signal path (or the two path endpoints) are near the boun-
   daries  of two latitudinal zones, a mix of the propagation predictions
   for the two latitudinal zones may be required to yield a more accurate
   representation of propagation conditions.  For example, if a transmis-
   sion were conducted between  Denver  and  Atlantic  City,  which  both
   border  as  low  and middle latitude locations, both of the charts for
   the low and middle latitude zones should  be  analyzed  and  mixed  in
   order  to  determine  the conditions which might be expected over that
   path.  Since the distances in this latter example are relatively small
   (compared  to  the latter examples), the northpoint of the signal path
   will not significantly affect propagation conditions.  This is why  we
   only  examined  the  latitude  of  the  startpoint  and endpoint.  For
   greater distances, the northpoint must be considered.



                             December 13, 1990





                                   - 14 -


   _2._9.  _V_H_F _P_r_o_p_a_g_a_t_i_o_n _P_r_e_d_i_c_t_i_o_n _C_h_a_r_t_s

        The prediction of potential VHF DX is not as simple as it is  for
   HF.  VHF signals have properties which are not usually affected by the
   ionospheric layers.  In our context, "VHF" will  be  considered  those
   frequencies  ranging  from  about  50 MHz to 220 MHz.  For information
   regarding the major types of VHF propagation which are possible,  con-
   sult part I of this document.

        A great deal of information can be extracted from the VHF predic-
   tion  charts.   Information  pertaining  to  HF communications is also
   imbedded in these charts.  As was done for the HF  prediction  charts,
   the  VHF  predictions are separated into three charts; one for each of
   the major latitude zones.

        The upper part of the chart forecasts the  quality  of  potential
   _d_i_s_t_a_n_t  _V_H_F  _s_i_g_n_a_l_s.   It  does  _n_o_t  depict  the quality of locally
   transmitted VHF signals.  This is  an  important  point  to  remember.
   Locally  transmitted  "line  of sight" signals can not be affected and
   are not affected by geomagnetic activity, auroral activity, or  SID's.
   Therefore,  only  the  distant  signals which can be affected by these
   phenomena are considered in these charts.

        As was the case with the other propagation prediction charts, the
   VHF  prediction charts are separated into groups of three 8-hour daily
   intervals.  However, the reference of time used  in  these  charts  is
   _L_O_C_A_L _t_i_m_e, _n_o_t UT time.  That is, the first line of each day in these
   charts represents the period between _l_o_c_a_l midnight  and  8  am  _l_o_c_a_l
   time.   This is the only major difference between these charts and the
   HF prediction charts.  It is also a very important diference.

        To use these charts, simply determine what time it is locally and
   examine  the  appropriate  day  in the charts and the appropriate plot
   line within that day.  The top portion of the prediction charts define
   the  quality  of  VHF  signals  which can be expected over larger dis-
   tances.  The bottom chart describes the  probability  of  experiencing
   conditions  capable  of  supporting  VHF DX.  Both charts use the same
   reference of time (local time).

        The  _S_I_D  _E_N_H_A_N_C_E_M_E_N_T  chart  at  the  upper  right-hand   corner
   describes  the  probability  of a SID (sudden ionospheric disturbance)
   temporarily enhancing VHF  communications.   The  probability  of  SID
   enhancements   increases  with  solar  activity,  but  decreases  with
   increasing latitude.  This data is also  of  value  to  the  HF  radio
   operator,  since  SID's almost always produce short-wave fades (SWF's)
   which can disrupt HF communications.  Since  SID's  are  sporadic  and
   very  unpredictable (due to the unpredictable nature of solar flares),
   they are predicted as percentages in these  charts.   SID-related  VHF
   enhancements  _d_o  _n_o_t occur on the dark-side of the earth.  Neither do
   SWF's.  Therefore, these SID prediction charts  _o_n_l_y  apply  to  those
   locations which are still illuminated by the sun.

        The _A_U_R_O_R_A_L _B_A_C_K_S_C_A_T_T_E_R prediction charts are of value to the VHF
   radio operator.  Auroral backscattering (as was described in part I of



                             December 13, 1990





                                   - 15 -


   this  document)  is  possible  at  VHF  frequencies  during  times  of
   increased  geomagnetic  and auroral activity.  These prediction charts
   define the approximate probabilities of VHF  propagation  via  auroral
   backscattering over the various latitudes.  VHF signals which are pro-
   pagated via aurora's can travel fairly large  distances.   Propagation
   via  aurora's  is  therefore considered a potential method of DXing on
   VHF  frequencies.   It  is,  however,  a  fairly  local  and  sporadic
   phenomena  and is usually not a widely-encountered form of propagation
   until auroral and geomagnetic activity reaches significant storm  lev-
   els.

        To make use of these VHF charts, simply consult  the  appropriate
   plot  lines  according  to  what day it is and the local time.  The HF
   operator may be able to determine what days will prove  less  reliable
   as  far  as day-time propagation goes by examining the probability for
   SID related SWF's.  Most SWF's, however, are only temporary and do not
   pose  a  significant  threat  to  most HF operators, unless the flares
   which produce them are particularly intense.

   _2._1_0.  _A_u_r_o_r_a_l _A_c_t_i_v_i_t_y _P_r_e_d_i_c_t_i_o_n_s

        Auroral activity is predicted for the three major latitude  zones
   identified  earlier.  Since the auroral zone itself is situated within
   the high-latitude zone, the high latitudes will  naturally  experience
   significantly more auroral activity than the middle and low latitudes.

        The prediction charts for auroral activity  are  most  useful  to
   those  people  interested  in  either observing auroral activity, pro-
   pagating radio signals using aurora's, or  for  people  interested  in
   determining  the extent of magnetic fluctuations occurring near area's
   of auroral activity.

        Since auroral activity migrates  equatorward  during  geomagnetic
   storms,  locations  which  may  usually be outside of the auroral zone
   itself may occasionally find themselves _i_n_s_i_d_e the auroral zone during
   periods  of  increased  geomagnetic  activity.   Likewise,  as auroral
   activity shifts equatorward, low latitudes may be able to begin  spot-
   ting the activity.

        These prediction charts can be used to determine whether  or  not
   potential  auroral  activity  may  be intense enough to be seen at low
   latitudes, or whether auroral activity will be dull  and  inactive  or
   bright and very active.

        To use the charts, simply examine the appropriate chart  (ie.  if
   you're  a middle latitude location, examine the middle-latitude chart)
   and select the column on the day you are most interested.   The  first
   plot line of each day represents the evening twilight period.  This is
   the period between when the sun sets and  before  the  sky  gets  com-
   pletely  dark.   The  second  plot line represents the midnight sector
   where the sky remains completely  dark  (excluding  effects  of  lunar
   phase).   The  last  plot  line  is  the  morning  twilight period and
   represents the time when the sky just barely begins to brighten  until
   the sun rises.



                             December 13, 1990





                                   - 16 -


        The phase of the moon is not taken into  consideration  in  these
   charts.   The  moon  can  have  a profound effect on the visibility of
   auroral activity, but does not affect auroral activity  itself.   That
   is,  just  because  the  moon  may  be  blocking  out light of auroral
   activity does not mean that  auroral  activity  is  not  in  progress.
   Indeed,  intense auroral storms can occur during a full moon as easily
   as they can during new moons.  Therefore, these charts  represent  the
   occurrence of auroral activity regardless of lunar phase.

        The intensity  of  auroral  activity  is  measured  according  to
   several  parameters.   Each  of  these parameters are discussed in the
   Glossary of Solar Terrestrial Terms.  In their most  basic  form,  the
   parameters  (low,  moderate, high, etc.) may be considered the bright-
   ness of auroral activity during dark-sky conditions  (ie.  periods  of
   new moon).  However, actual visual movements, color changes and aerial
   extent are also considered when classifying auroral activity in  these
   prediction charts.



   _3.  _M_o_n_t_h_l_y _S_o_l_a_r _T_e_r_r_e_s_t_r_i_a_l _R_e_v_i_e_w

        Every month, statistics and information regarding solar and  ter-
   restrial  activity  for  the preceding month are gathered and compiled
   into a document called the _M_o_n_t_h_l_y  _S_o_l_a_r  _T_e_r_r_e_s_t_r_i_a_l  _R_e_v_i_e_w.   This
   document  contains  not  only  information  regarding  the  nature  of
   activity of solar  and  geophysical  phenomena  during  the  preceding
   month, but also includes a six month solar cycle outlook.  This can be
   of great value to the radio operator who is interested in  determining
   what  conditions  might be like six months down the road.  It can also
   be of interest to the astronomer who may enjoy searching  for  auroral
   activity or solar flares.

        In addition to the written summary, a statistical summary of  the
   previous  month is given in tabular form, summarizing all of the major
   solar parameters (ie.  solar  flux,  sunspot  numbers,  active  region
   sizes, numbers and types of flares, etc.).

        This report is intended to serve as a general  summary  regarding
   activity  and phenomena encountered during the previous month.  It can
   provide some interesting results if data from the report is charted or
   graphed or statistically analyzed.



   _4.  _G_e_o_m_a_g_n_e_t_i_c _S_t_o_r_m _A_l_e_r_t

        This alert is posted over the nets whenever magnetic storm condi-
   tions  reach or exceed minor storm levels over middle latitudes.  This
   alert may be preceded by a warning if a magnetic storm is expected  to
   occur but hasn't yet begun.

        If storm conditions are expected to significantly alter the accu-
   racy  of  the  forecasts  given  earlier in the week, a revised set of



                             December 13, 1990





                                   - 17 -


   forecast charts may be included with this alert.   The  revised  fore-
   casts follow exactly the same format as has been described in the pre-
   vious sections and so can be interpreted and used in the same ways  as
   was described above.

        Rarely, a magnetic storm may occur with particularly intense mag-
   netic  fluctuations.   If these fluctuations become significant enough
   to begin influencing ground-based systems, an Electrical Anomaly Warn-
   ing  may be included within this alert.  That is, if magnetic fluctua-
   tions become intense enough to  begin  inducing  potentially  damaging
   electrical currents in ground-based conductive networks, a warning may
   be posted along with this alert to  warn  of  the  potential  magnetic
   interactions  that  might  occur.   These  warnings are rare, however.
   Magnetic storms rated as "severe" are generally required  before  mag-
   netic  fluctuations  are  able  to  reach the intensities necessary to
   induce electrical currents in ground-based systems.



   _5.  _C_o_n_c_l_u_d_i_n_g _R_e_m_a_r_k_s

        The solar terrestrial reports which are posted over the  networks
   contain a great deal of information.  Understanding them may take some
   time.  Applying the  information  contained  in  them  may  take  even
   longer.   This  document (part I and II) was developed to help explain
   the nature and format of these reports.  It was also developed to help
   those  who are interested in interpreting and applying the information
   contained in the reports.

        It is hoped that this document will help those who are interested
   in  better  understanding  the  solar  terrestrial reports.  Questions
   and/or comments are welcome.  If any further explanations are required
   which  have not been adequately covered in this document, feel free to
   send an inquiry to "std_oler@hg.uleth.ca".

        We have learned a great deal over the years regarding the impacts
   of  solar  activity  on  our terrestrial sphere.  But there is still a
   great deal more we need to learn before we can expect  to  master  the
   art  of  predicting  the  impacts of solar activity on the earth.  Our
   curiosity drives us further and our lust for  knowledge  quickens  our
   pace of learning.  With developements of new devices and technologies,
   we are steadily edging closer to understanding  both  our  terrestrial
   environment and the vast environment of space.  The educational insti-
   tutions and research organizations are the backbones of our  knowledge
   and  growth.   We  must  therefore respect these institutions, support
   them, and encourage them so that our body of knowledge is able to con-
   tinue expanding into the limitless realm of science.










                             December 13, 1990





                                   - i -





                             Table of Contents




   Introduction ....................................................    1

   The Solar Terrestrial Forecast and Review .......................    2

   Summary of Solar Terrestrial Activity ...........................    2

   Short Term Solar Terrestrial Forecast ...........................    5

   Solar Region Summary ............................................    6

   Geomagnetic Activity Summary ....................................    8

   10-Day Geomagnetic Activity Forecast ............................    9

   Graphical Analysis of Solar Activity ............................   10

   20-Day Solar Activity Forecast ..................................   10

   HF Radio Signal Propagation Predictions .........................   11

   VHF Propagation Prediction Charts ...............................   14

   Auroral Activity Predictions ....................................   15

   Monthly Solar Terrestrial Review ................................   16

   Geomagnetic Storm Alert .........................................   16

   Concluding Remarks ..............................................   17




















                             December 13, 1990